## Slide 1: A very short overview on the Off-Axis Holography System

## Slide 2
Tunable Laser Source for Wavelength Selectivity
Make sure you have code (ask me) that connects to these 4 things:
Motorized Polarization Paddle
Fiber Switch Control For Lantern Legs
Physical Requirements
  Make sure the reference beam is polarized correctly using the manual paddles
  Use Red Light checker through one leg for coarse alignment to camera
Bonus: Use a power meter if you want to measure transmission, but you’d have to calibrate insertion loss through all of the switch ports and hope the connectors are good
Camera Frame Grabber
Polarizer
InGaAs Camera
Beam Splitter
Beam Expander
Laser Source
Optical Switch
Photonic Lantern
Lens
10:90 Splitter
Polarization Paddles Go Here

## Slide 3
For each leg:
Select Leg
Loop can be adjusted, but I would have the slowest moving part on towards the outside of the loop, testing should be done to figure out appropriate wait times
Start
Connect All Software
For each 𝜆:
Select Wavelength
Are Fringes Visible?
Change Polarization
nah
Record Image
Was that all wave- lengths?
yea
nah
Was that all the legs?
nah
yea
yea
Dope
Save images something like:
(leg)##-(wavelength)####.npy
Wait
Wait
This may need to be done manually depending on switch
Workflow for Data Collection:

## Slide 4
Find Centroids of Twin Images in FFT
Start
Load Data Set
Save Ideal Parameters
Optimize Parameters [X/Y Offset, Diameter, Phase Factor]
Dope
Workflow for Data Processing:
Find Center of Field
Note: Centroid locations are wavelength dependent
Find Ballpark Quadratic Phase Error
Find (or calculate) Ballpark Mode Field Sizes
Save Decomp and Recovered Fields
Note: This is a very involved process that can use improvement. I will share example code, but the idea is you compare a field constructed of idealized modes with your data and try for the closest match.
Set LP01 Phase to 0
Make fun plots